## Slide 1: Fire and Smoke Detection: Choosing the Model
Stage 1: three backbones and two detection heads compared over 40 training epochs
DINOv3 | MobileNetV3-Large | ResNet-18 | Faster R-CNN | FCOS
Notes: Introduce the project: an industrial fire and smoke detector for fixed cameras. Today covers stage 1 only: how we compared the candidate models and why we continue with DINOv3 plus Faster R-CNN.

## Slide 2: The problem: fire and smoke on industrial cameras, around the clock
1
Poor light, high cameras
Cameras are mounted high in dim industrial lighting, with glare and reflections
2
Runs 24 hours a day
False alarms must be very rare, or operators stop trusting the system
3
Fire can be hidden
A flame behind equipment may show only as a glow on nearby surfaces
4
Smoke and fire
Two classes to detect; smoke has no fixed shape or edge
5
Small, distant fires
A fire far from the camera covers only a few pixels
6
About 70 cameras
At least 10 frames per second overall: speed and size matter too
Question for stage 1: which backbone and which detection head should the detector be built on?
Notes: Six requirements from the site. The second one drives most decisions: because the system runs 24/7, the false-alarm rate is as important as accuracy. Stage 1 answers one question with measurements: which backbone and which head.

## Slide 3: Approach: one detector, with two parts to choose
Same data
D-Fire: 13,776 training, 3,445 validation and 4,306 test images; 45% contain no fire or smoke
Same training
40 epochs, AdamW, learning rate 1e-4, batch 8, same augmentation; backbone frozen
Same measures
After every epoch: mAP@0.5, and detections at no more than 1% false alarms
Notes: The detector has a backbone that extracts features, a feature pyramid for different object sizes, a detection head that outputs boxes, and a scene classifier for hidden fire. We compare three backbones and two heads. To keep it fair, everything else is identical. The backbone is frozen in stage 1, so we measure how good each backbone's ready-made features are.

## Slide 4: Three backbone candidates
DINOv3 ViT-S/16
Vision Transformer
21.6M
backbone parameters
Structure 12 transformer blocks
Pretraining Self-supervised, no labels, 1.689 billion images
+ Strongest general features; sees the whole image
- Slowest; needs a pyramid built on top
MobileNetV3-Large
Convolutional network for mobile devices
2.95M
backbone parameters
Structure 15 inverted-residual blocks
Pretraining Supervised, ImageNet-1k, 1.28 million images
+ Smallest and about 2.5 times faster
- Local view; more false alarms
ResNet-18
Convolutional network with skip connections
11.2M
backbone parameters
Structure 8 residual blocks, 20 convolutions
Pretraining Supervised, ImageNet-1k, 1.28 million images
+ Simple, standard, supported everywhere
- Lowest accuracy of the three
Notes: DINOv3 is a Vision Transformer trained by Meta without labels on 1.689 billion images. MobileNetV3 and ResNet-18 are convolutional networks trained with labels on ImageNet, about 1,300 times fewer images. Parameters shown are for the backbone alone; the detection head adds about 14.5 million to each.

## Slide 5: Inside DINOv3 ViT-S/16
Input
3 x 640 x 640 image
Patch embedding
16 x 16 px patches
1,600 tokens x 384
12 transformer blocks
every token attends to every
other token (6 heads)
Feature map
1,600 tokens x 384
(1/16 resolution)
Feature pyramid
4 levels, 256 channels
80, 40, 20, 10
Inside one transformer block (repeated 12 times)
LayerNorm
Self-attention
6 heads
+ skip
LayerNorm
MLP
384 > 1,536 > 384
+ skip
21.6M
parameters
12
transformer blocks
1.689 B
training images, no labels
Advantages
Best features with the backbone frozen
Global context from the first block
Disadvantages
About 900 ms per frame on CPU
One scale only; cost grows fast with image size
Our training: backbone frozen; blocks 6, 9, 10 and 12 feed the pyramid.
Notes: The image is cut into 16 by 16 pixel patches, giving 1,600 tokens. Twelve transformer blocks let every token look at every other token, so each patch is described in the context of the whole image. That global view helps with smoke. The output is a feature map, not boxes, so we build a four-level pyramid from four of the blocks and add a detection head.

## Slide 6: Inside MobileNetV3-Large and ResNet-18
MobileNetV3-Large: 2.95M parameters, 15 inverted-residual blocks, 62 convolutions
Input
640 x 640
Stem
3x3 conv
16 ch
Stages 1-2
3 blocks
24 ch, 160x160
Stage 3
3 blocks
40 ch, 80x80
Stages 4-5
6 blocks
112 ch, 40x40
Stages 6-7
3 blocks
960 ch, 20x20
Pyramid
FPN
4 levels
One block: 1x1 conv (expand) > depthwise conv > squeeze-and-excite > 1x1 conv (project) > + skip. Cheap by design: built for phones.
ResNet-18: 11.2M parameters, 8 residual blocks, 20 convolutions
Input
640 x 640
Stem
7x7 conv
+ max-pool
layer1
2 blocks
64 ch, 160x160
layer2
2 blocks
128 ch, 80x80
layer3
2 blocks
256 ch, 40x40
layer4
2 blocks
512 ch, 20x20
Pyramid
FPN
4 levels
One block: 3x3 conv + BatchNorm > ReLU > 3x3 conv + BatchNorm > + skip > ReLU. The skip connection is what made deep networks trainable.
Both: pretrained on ImageNet-1k with labels; frozen in stage 1; the 80x80, 40x40 and 20x20 maps feed a standard Feature Pyramid Network.
Notes: Both are convolutional networks that shrink the image step by step while adding channels, so they produce several scales naturally. MobileNetV3 uses depthwise convolutions to stay cheap. ResNet-18 uses plain 3 by 3 convolutions with skip connections. Each layer sees only a local neighbourhood, unlike the transformer.

## Slide 7: Two detection heads: Faster R-CNN and FCOS
Faster R-CNN: two stages, 14.5M parameters, 4 losses
Pyramid
4 levels
Stage 1: proposals
6 anchor boxes per location:
object or not?
~300 proposals
after NMS
RoIAlign
crop each to 7x7
Stage 2: box head
2 FC layers:
class + refined box
Output
boxes, class,
score
+ most accurate; clean scores, so a strict threshold (0.90) works - large head; cannot be exported as one batch for many cameras
FCOS: one stage, no anchors, 0.60M parameters, 3 losses
Pyramid
8,500 locations
Two conv towers
classification tower
regression tower
Every location predicts
class score, 4 box distances,
centre-ness
Score
sqrt(class x centre-ness)
top 300, NMS
Output
boxes, class,
score
+ simple, 24 times smaller head; fixed-size output, so many cameras can be batched - compressed scores (max about 0.75); lower accuracy as trained
Both read the same 4-level feature pyramid and output the same thing: boxes with a class and a score. Only the way they get there differs.
Notes: Faster R-CNN works in two stages: a proposal network suggests about 300 regions, then a box head examines each one. That second look gives well-separated scores. FCOS has no proposals and no anchors: every location predicts a class, a box and a centre-ness value directly. It is simpler and can be batched across cameras, but its scores are compressed.

## Slide 8: Results: DINOv3 leads at every one of the 40 epochs
Chart: Validation mAP@0.5 after each epoch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
DINOv3 ViT-S + Faster R-CNN | 0.44937 | 0.5232 | 0.54173 | 0.57711 | 0.59449 | 0.60207 | 0.61651 | 0.62364 | 0.62066 | 0.64034 | 0.64661 | 0.66139 | 0.6711 | 0.66912 | 0.6717 | 0.68062 | 0.68485 | 0.68341 | 0.68731 | 0.69482 | 0.69686 | 0.69754 | 0.70926 | 0.70824 | 0.70976 | 0.71336 | 0.71658 | 0.71666 | 0.7219 | 0.72236 | 0.72276 | 0.72734 | 0.72529 | 0.72813 | 0.72842 | 0.72892 | 0.72881 | 0.7312 | 0.72947 | 0.72967
MobileNetV3-L + Faster R-CNN | 0.3705 | 0.45906 | 0.50079 | 0.52168 | 0.53691 | 0.54179 | 0.5766 | 0.57704 | 0.60259 | 0.60464 | 0.60907 | 0.61113 | 0.62596 | 0.63524 | 0.64043 | 0.63811 | 0.64772 | 0.65049 | 0.6537 | 0.65519 | 0.65915 | 0.66191 | 0.67032 | 0.67397 | 0.67947 | 0.67872 | 0.68169 | 0.68994 | 0.68898 | 0.69389 | 0.69259 | 0.69443 | 0.70017 | 0.69804 | 0.70111 | 0.70504 | 0.70313 | 0.70303 | 0.70559 | 0.70404
ResNet-18 + Faster R-CNN | 0.2553 | 0.31331 | 0.40562 | 0.42513 | 0.45898 | 0.47499 | 0.48045 | 0.49395 | 0.50657 | 0.53325 | 0.53341 | 0.53956 | 0.54846 | 0.55231 | 0.57099 | 0.58098 | 0.58834 | 0.5961 | 0.59731 | 0.59592 | 0.60789 | 0.60888 | 0.61186 | 0.62536 | 0.61761 | 0.62695 | 0.63562 | 0.63907 | 0.63565 | 0.6382 | 0.64648 | 0.64518 | 0.64909 | 0.65042 | 0.65381 | 0.65658 | 0.65384 | 0.65593 | 0.65673 | 0.65656
DINOv3 ViT-Ti + FCOS | 0.3117 | 0.37936 | 0.40471 | 0.42441 | 0.45276 | 0.45486 | 0.48607 | 0.4963 | 0.51175 | 0.52592 | 0.51719 | 0.52591 | 0.52629 | 0.54692 | 0.55534 | 0.5432 | 0.55108 | 0.56392 | 0.55062 | 0.5635 | 0.58061 | 0.57153 | 0.58017 | 0.57522 | 0.58023 | 0.58014 | 0.59402 | 0.59215 | 0.60008 | 0.60068 | 0.59914 | 0.60601 | 0.60949 | 0.60935 | 0.61028 | 0.61628 | 0.61784 | 0.61484 | 0.62125 | 0.61957
Model | Best val | Test
DINOv3 ViT-S | 0.7312 | 0.7196
MobileNetV3-L | 0.7056 | 0.6968
ResNet-18 | 0.6567 | 0.6477
ViT-Ti + FCOS | 0.6212 | 0.6125
mAP@0.5
Same head, same data, same settings: only the backbone differs
DINOv3 is 2.3 points ahead of MobileNetV3 and 7.2 ahead of ResNet-18 on test
No model overfitted: all four were still improving at epoch 40; the smaller ones underfit
Notes: Validation mAP after each of the 40 epochs. The order DINOv3, MobileNetV3, ResNet-18 holds at every epoch. The three Faster R-CNN models train almost the same number of parameters, so the difference comes from the frozen backbone features. On overfitting: none of the models overfitted. Validation accuracy was still rising at the end for all four, and the best epoch was 38 or 39. The smaller models underfit instead: ResNet-18 ends with the highest training loss, and the FCOS model trains only 1.5 million parameters. Note for questions: DINOv3's numbers were recorded before a test-time speed setting was changed, which costs about 0.005 mAP, so its lead is about half a point smaller than shown. It still leads clearly.

## Slide 9: Results: false alarms, speed, and the two heads
Model | Detected at 1% false alarms | False-alarm rate | CPU ms / frame | Parameters
DINOv3 ViT-S + Faster R-CNN | 86.9% | 0.37% | 894-912 | 39.3M
MobileNetV3-L + Faster R-CNN | 86.9% | 0.87% | 346-385 | 20.0M
ResNet-18 + Faster R-CNN | 67.9% | 0.87% | 414 | 27.9M
DINOv3 ViT-Ti + FCOS | 74.2% | 0.56% | 338-398 | 6.95M
Validation images; threshold raised until at most 1% of fire-free images trigger a detection. CPU time on the project laptop.
False alarms
DINOv3 and MobileNetV3 detect the same share of fire/smoke images, but DINOv3 needs less than half the false alarms (0.37% against 0.87%)
Speed
MobileNetV3 is about 2.5 times faster than DINOv3. ResNet-18 is slower than MobileNetV3 and less accurate
Faster R-CNN and FCOS
On the same backbone FCOS is not faster (924 ms against 884 ms). Its gain is batched export for many cameras; its scores top out near 0.75
Notes: For an alarm system the key number is how many fires are detected while false alarms stay under 1%. DINOv3 and MobileNetV3 both detect about 87%, but DINOv3 does it at 0.37% false alarms against 0.87%. ResNet-18 detects only 68%. On the heads: the FCOS model here also uses a smaller backbone, so its lower accuracy is not due to the head alone. What we measured on the same backbone is speed and export: FCOS is not faster, but it can be exported as one batch.

## Slide 10: Decision: continue with DINOv3 + Faster R-CNN
1
Most accurate
Best mAP on validation and test, on both smoke and fire
2
Fewest false alarms
Same detections as MobileNetV3 at less than half the false-alarm rate
3
Features work without training
Best result with every backbone frozen
4
Clean scores
Faster R-CNN keeps a strict 0.90 threshold usable
0.7312
validation mAP@0.5
0.7196
test mAP@0.5
86.9%
detected at 0.37% false alarms
What it costs: about 900 ms per frame on CPU and no batched export. MobileNetV3 (2.5 times faster) and FCOS (batchable) are kept for the fast version; ResNet-18 is dropped.
Notes: Four reasons. It is the most accurate. It gives the fewest false alarms for the same detections, which is the central requirement. Its features are the best even without training them. And Faster R-CNN gives clean scores. The cost is speed and export, which concern deployment, so accuracy is settled first and MobileNetV3 and FCOS are kept for a fast version.

## Slide 11: Next goals
1
Fine-tune the backbone (stage 2)
Unfreeze the last 2 transformer blocks at a 20 times lower learning rate
2
Small and distant fires
Higher input resolution and scale augmentation
3
Hard-negative training
Hard hats, hi-vis clothing, lamps and haze labelled as 'not fire'
4
Video testing
Industrial footage with temporal confirmation: 6 detections in 15 frames
5
A fast version for 70 cameras
MobileNetV3 backbone and FCOS head, exported for GPU batching
6
Data from the site's own cameras
Labelled with one consistent rule
Documents: project log, model selection report (21 pages, results of every epoch), training report, technical and research report, source code
Notes: The plan from here. First fine-tune part of the DINOv3 backbone at a low learning rate, which is where overfitting must be watched. Then small and distant fires, hard negatives to push false alarms down, testing on video, a fast version for the 70-camera requirement, and data from the site's own cameras. The full report has the results of every epoch for every model.